MR   MANUAL Command Version

300 MHz Bruker Sample Xpress

- Login to computer and double-click on the icon to open TopSpin3.2

- Place your sample tube in a spinner carefully using a Kim Wipe (do not touch spinner with your fingers!)  Set the correct depth with the depth gauge.

- On the SampleXpress key pad, touch Add, Go To Free.  Insert your sample into the SampleXpress.

- In TopSpin, type sx #, where # is the holder number corresponding to your sample (a space is between sx and #).  When the SampleXpress light turns green, you may proceed.

- Type new and enter a file name, select an experiment, and click OK.

- Type lock and select your solvent.

- Type topshim to automatically perform gradient shimming.

- Type atma to automatically tune and match.

- Type rga to set the receiver gain. (You may skip this step if running 13C)

- Type zg to begin data acquisition.

- When your experiment has finished, you can process your data as desired. (efp –Exponential multiply/Fourier transform,Phase, apk –Autophase, cal –Calibrate, PeakPick, Integrate, Plot)

- Type sx ej to eject your sample from the magnet.

- On the SampleXpress key pad, touch Remove, Go To Position, and select your Holder Number.  Remove your sample and spinner.

- Logout by clicking the  button at the top of the screen.