MR   ICON Command Version

300 MHz Bruker Sample Xpress

- Login to computer and double-click on the icon to open TopSpin3.2

- Click the Icon button or type icon in the command line, then click Automation.  Follow the prompts for username and password entry.

- Place your sample tube in a spinner carefully using a Kim Wipe (do not touch spinner with your fingers!)  Set the correct depth with the depth gauge.

- On the SampleXpress key pad, touch Add, Go To Free.  Insert your sample into the SampleXpress.

- Scroll to your Holder Number in the Icon NMR window, and double click on your Holder Number.

- Enter a Name.  Select a Solvent and Experiment using the dropdown menus.  Enter a Title. [Note: to add an experiment to the same sample, right click on the Holder Number, click Add]

- Click on your Holder Number to highlight it, and click Submit.

- When the experiment has finished, double-click on your Experiment in the “Preceding Experiments” section of IconNMR.  This will open your spectrum in TopSpin.  You can now process your data in TopSpin as desired. (efp –Exponential multiply/Fourier transform,Phase, apk –Autophase, cal –Calibrate, PeakPick, Integrate, Plot)

- On the SampleXpress key pad, touch Remove, Go To Position, and select your Holder Number.  Remove your sample and spinner.

- Logout by clicking the  button at the top of the screen.